## Slide 1: معماری کامپیوتر پیشرفته
وحید حقیقت دوست
haghighatdoost@shahed.ac.ir
http://ref.shahed.ac.ir/haghighatdoost
دانشکده فنی و مهندسی
فصل اول-مقدمه

## Slide 2: بارم بندی
آزمون پایان ترم: 11 نمره
آزمون میان ترم: 5 نمره
ارائه:4 نمره
  تعیین موضوع ارائه حداکثر تا پایان مهر
  از ابتدای آذر ماه تا یک هفته مانده به پایان ترم
  ارائه ها در جلسات کلاس درسی و برای کلیه دانشجویان کلاس باید انجام شود
مقاله: 3 نمره
  تا یک هفته پس از آزمون پایان ترم باید مستندات مربوط به ارسال مقاله ارائه شود.
موضوعات ارائه و مقالات تحقیقاتی:
  مدیریت کش
    اولویت بندی خارج نمودن اطلاعات قدیمی از کش
    سیاست گذاری مناسب برای جابجایی اطلاعات بین سطوح مختلف کش
  مدیریت پیش واکشی
    پیش بینی دستورات جهت دیکدینگ پیش از رویداد
  چند پردازندگی
    راهکارهای افزایش سرعت پردازش با افزایش تعداد هسته ها
    ایجاد شبکه ای از هسته ها
  تاثیر مدارات محاسباتی خاص در کارایی پردازنده ها
    استفاده از واحدهای محاسباتی
  طراحی کامپایلرها برای افزایش بهره وری از توانمندی پردازنده ها

## Slide 3: طرح کلی دوره
معرفی
سلسله مراتب حافظه (Memory Hierarchy)
پیش واکشی (Prefetching)
موازی سازی در سطح دستور العمل (Instruction-level parallelism)
  Pipeline, branch prediction, out-of-order execution, …
موازی سازی داده ها (Data-level parallelism)
پردازنده های برداری و SIMD (Vector processors and SIMD)
موازی کاری ریسمان ها (Thread-level parallelism)
  پروتکل های چند هسته ای و پروتکل های انسجام (Multicores and coherency protocols)

## Slide 4: فصول درسی
فصل اول
  Fundamentals of Quantitative Design and Analysis
فصل دوم
  Memory Hierarchy Design
فصل سوم
  Instruction-Level Parallelism and Its Exploitation
فصل چهارم
  Data-Level Parallelism in Vector, SIMD, and GPU Architectures
فصل پنجم
  Thread-Level Parallelism

## Slide 5: منابع درسی
Computer Architecture: A Quantitative Approach, 6th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019

## Slide 6: مالکیت معنوی
Lectures adopted from Computer Architecture: A Quantitative Approach, 6th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Lecture notes of Dr. Hamed Farbeh, Department of Computer Engineering Amirkabir University of Technology

## Slide 7: معماری کامپیوتر چیست؟
Application
Physics
In its broadest definition, computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
(but there are exceptions, e.g. magnetic compass)
طراحی لایه های انتزاعی
با استفاده از فن آوری های تولید موجود معمار کامپیوتر نمیتواند در تکنولوژی دخالت کند
شکاف آنقدر بزرگ است که نمی تواند در یک مرحله برطرف شود
فاصله Application تا Physics قطب نما یک لایه است.
هر آنچه که طراح می سازد، منتج به یک Application میشود.
ماده اولیه یا پایین ترین سطح طراحی

## Slide 8: Abstraction Layers in Modern Systems
Algorithm
Gates/Register Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
در دنیای کامپیوتر فاصله Application تا Physics بسیار زیاد است.

## Slide 9
Computing Devices Then…
EDSAC, University of Cambridge, UK, 1949

## Slide 10
Computing Devices Now
Robots
Supercomputers
Automobiles
Laptops
Set-top boxes
Smart phones
Servers
Media Players
Sensor Nets
Routers
Cameras
Games

## Slide 11: معماری به طور مداوم در حال تغییر است
Architecture continually changing
Compatibility
Cost of software development makes compatibility a major force in market
Applications
Technology
Applications suggest how to improve technology, provide revenue to fund development
Improved technologies make new applications possible
سوال: آیا کاربرد است که تکنولوژی را پیش میبرد یا تکتولوژی هست که کاربرد را تعریف میکند
در توسعه گام به گام کاربرد و تکنولوژی باید به سازگاری (Compatibility) توجه داشته باشیم. یعنی سخت افزار جدید باید به گونه ای باشد که کاربردهای قدیمی روی آن اجرا شوند و یا کاربردهای جدید به گونه ای باشند که روی سخت افزار قدیمی هم اجرا شوند.

## Slide 12
[from Kurzweil]
Major Technology Generations
Bipolar
nMOS
CMOS
pMOS
Relays
Vacuum Tubes
Electromechanical
?
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Moore's law is the observation that the number of transistors in a dense integrated circuit (IC) doubles about every two years.

## Slide 13: Single-Thread Processor Performance

## Slide 14: تحول در طراحی کامپیوتر
از سال 1950 در طی50 سال اول، قانون مور حاکم بود
  بهبود فناوری باعث بهبود مستمر عملکرد میشد
  بدون تغییر مدلهای نرم افزاری، انرژی بهبود پیدا میکرد
  برنامه نویسان سطوح مختلف برای پیاده سازی برنامه ها ارائه میکردند
  چشم امید نرم افزار کاران به بهبود سخت افزار بود
در دو دهه اخیر، تکنولوژی ساخت (کلاک را بالا بردن و تعداد ترانیزیستورها را افزایش دادن و...) مقیاس بندی فناوری کند (متوقف) شد
Upheaval in Computer Design

## Slide 15: تحول در طراحی کامپیوتر (ادامه..)
این سد بزرگ دنارد اسکیلینگ (Dennard Scaling) بود.
دنارد گفت که با پیشرفت تکنولوژی Power density ثابت میماند و ارتباطی با تکنولوژی ندارد.
اگر تعداد ترانزیستور در واحد سطح افزایش یابد (مور)، میزان مصرف انرژی ثابت میماند (دنارد).
بنابراین باکوچک شدن ابعاد ترانزیستور ولتاژ و جریان کم میشد لذا میتوانستیم ابعاد را کم کنیم که طبق قانون دنارد مصرف انرژی ثابت باقی میماند.
ولتاژی که یک زمانی 5 ولت بود به مرور کم شد و به 3 ولت رسید و الان به 1.3 رسیده است.
Dennard Scaling
Robert Dennard (born September 5, 1932) is an American electrical engineer and inventor

## Slide 16: تحول در طراحی کامپیوتر (ادامه..)
هیچ جایگزینی رقابتی برای CMOS به این زودی ها وجود ندارد
در تکنولوژی CMOS از یک حدی نمیتوان ولتاژ را کمتر کرد (ولتاژ آستانه این محدودیت را برای ما ایجاد میکند).
برای توسعه سخت افزار لازم است تا ترانزیستورها در واحد سطح افزایش یابد و از آنجا که در واحد سطح دیگر پاور ثابت نمیماند، لذا گرمای تولید شده افزایش می یابد.
با افزایش دما، ولتاژ آستانه بالاتر میرود.
مدیریت گرما در طراحی پردازنده ها از چالش های امروز است.
No new technology after CMOS

## Slide 17: تحول در طراحی کامپیوتر (ادامه..)
افزایش فرکانس تا کجا پیش میرود؟
  تکنولوژی به ما اجازه میدهد که فرکانس بالا داشته باشیم ولی گرمای تولید شده در واحد سطح افزایش می یابد
از حدود سال 2012 فرکانس CPU ها در حد 3 گیگا هرتز باقی مانده است.
افزایش تعداد ترانزیستورها باعث افزایش دما میشود.
بهره وری انرژی همه چیز را محدود می کند
About frequency increase

## Slide 18: تحول در طراحی کامپیوتر (ادامه..)
برخی اعتقاد دارند که قانون مور به انتها رسیده است.
  مور گفته بود که هر دو سال تعداد ترانزیستورها در واحد سطح دو برابر میشود.
زمانی ترانزیستورها در حد 10 میکرون بودند بعد شد 1 میکرون و ...
در حال حاضر خیلی از تراشه ها تکنولوژی 10 و یا 14 نانو هستند.
  پایه ها، لایه اکسید، لایه metal, source, drain , …
  TSMC, Intel , Sumsung توانمندترین شرکت های سازنده ترانزیستور هستند.
افزایش تعداد ترانزیستورها در واحد سطح باعث افزایش دما میشود.
بهره وری انرژی همه چیز را محدود می کند
Technology constraints..

## Slide 19: تحول در طراحی کامپیوتر (ادامه..)
مسیری که در حال حاضر پیش رو است، معماری کامپیوتر است.
قانون دنارد به انتها رسیده است.
  در حال حاضر به حداکثر توان مصرفی
  و حداکثر گرمای قابل قبود در سطح رسیده ایم.
در این درس میخواهیم ببینیم که یک معمار کامپیوتر چطور میتواند از یک احود پرازش به نحوه ای استفاده کند که کارایی افزایش یابد.
در حال حاضر مصرف انرژی دغدغه اصلی یک معمار کامپیوتر است
  به هر قیمتی نمیخواهیم کارایی را بالا ببریم.
دیگر برنامه نویسان نمیتوانند مصرف کننده باشند. باید برنامه نویسان خودشان را با تکنولوژی همگام کنند :
  سیستم های موازی: تغییر از Single core به Multi core و یا پردازنده های GPU
  سیستم های ناهمگن: برنامه نویس نمیتواند سخت افزار را بصورت بلاک باکس ببیند. پردازنده های خاص منظوره در کنار پردازنده اصلی حضور دارند.
Computer Architecture…

## Slide 20: دسته بندی کامپیوترهای امروزی
Mobile (smartphone/tablet)
  >1 billion sold/year
  Market dominated by ARM-ISA-compatible general-purpose processor in system-on-a-chip (SoC)
  Plus sea of custom accelerators (radio, image, video, graphics, audio, motion, location, security, etc.)
  همه این اجزا بصورت یک IC ارائه میشود
Warehouse-Scale Computers (WSCs)- کامپیوترهای سرور
  100,000’s cores per warehouse
  Market dominated by x86 , x64-compatible server chips
  Dedicated apps, plus cloud hosting of virtual machines
  Now seeing increasing use of GPUs, FPGAs, custom hardware to accelerate workloads (برای افزایش کارایی)
Embedded computing (هر تجهیزی که کار پردازشی انجام میدهد)
  Wired/wireless network infrastructure, printers
  Consumer TV/Music/Games/Automotive/Camera/MP3
  Internet of Things!

## Slide 21: Computer Architecture: A Little History
Why worry about old ideas?
Those who ignore history are doomed to repeat it
Helps to illustrate the design process, and explains why certain decisions were taken
Because future technologies might be as constrained as older ones

## Slide 22: Changing Face of Computing
1960s: mainframes
1970s: mini-computers
1980s: Desktop computers
  Desktop
  Workstation
   Servers
    Reliable
    Long term file storage and access
    Larger memory
    More computing power
1990s: Embedded, Internet
  PDA
  Set top boxes, Game consoles
2000s:
  ? (multi-core, networked, ..)
  Personal Mobile Devices
  Clusters / Cloud
چالش های ما در دهه های مختلف متفاوت بودند
Notes: What are mainframes?
Who produces them?
Are they dead now?

## Slide 23: کامپیوترهای آنالوگ
Analog Computers
این کامپیوترها، متغیرهای مساله را بصورت کمیت های فیزیک نمایش میدهند و از رفتارهای فیزیکی مقیاس شده برای نتایج محاسبات استفاده میکنند
[Marsyas, Creative Commons BY-SA 3.0]
Antikythera mechanism c.100BC
[BenFrantzDale, Creative Commons BY-SA 3.0]
Wingtip vortices of Cessna tail in wind tunnel

## Slide 24: کامپیوترهای دیجیتال
Digital Computers
متغیرهای مسئله را به صورت اعداد گسسته نشان داده میشوند
  مقادیر گسسته، در مقابل نویز ایمن هستند
محاسبات دقیق و قطعی را حاصل می کند
  ورودی های مشابه دقیقاً خروجی های یکسانی را ارائه می دهند
محدود به عملکردهای قابل تحقق فیزیکی نیست
  هر الگوریتمی که قابل بیان باشد، توسط کامپیوتر قابل انجام است

## Slide 25: Charles Babbage (1791-1871)
Lucasian Professor of Mathematics, Cambridge University, 1828-1839
A true “polymath” with interests in many areas
  Frustrated by errors in printed tables, wanted to build machines to evaluate and print accurate tables
Inspired by earlier work organizing human “computers” to methodically calculate tables by hand

## Slide 26: Difference Engine 1822
Continuous functions can be approximated by polynomials, which can be computed from difference tables:
  f(n) = n2 + n + 41
  d1(n) = f(n) – f(n-1) = 2n
  d2(n) = d1(n) – d1(n-1) = 2
Can calculate using only a single adder:
n
d2(n)
d1(n)
f(n)
0
41
1
2
2
2
3
2
4
2
4
6
8
43
47
53
61

## Slide 27: تحقق ماشین محاسبه تفاضلی
Mechanical calculator, hand-cranked, using decimal digits
Babbage did not complete the DE, moving on to the Analytical Engine (but used ideas from AE in improved DE 2 plan)
Schuetz in Sweden completed working version in 1855, sold copy to British Government
Realizing the Difference Engine

## Slide 28: موتور تحلیلی 1837
Analytical Engine 1837
Recognized as first general-purpose digital computer
  Many iterations of the design (multiple Analytical Engines)
Contains the major components of modern computers:
  “Store”: Main memory where numbers and intermediate results were held (1,000 decimal words, 40-digits each)
  “Mill”: Arithmetic unit where processing was performed including addition, multiplication, and division
  Also supported conditional branching and looping, and exceptions on overflow (machine jams and bell rings)
  Had a form of microcode (the “Barrel”)
Program, input and output data on punched cards
Instruction cards hold opcode and address of operands in store
  3-address format with two sources and one destination, all in store
Branches implemented by mechanically changing order cards were inserted into machine
Only small pieces were ever built

## Slide 29: انتخاب موتورهای تحلیلی
Analytical Engine Design Choices
Decimal, because storage on mechanical gears
  Babbage considered binary and other bases, but no clear advantage over human-friendly decimal
40-digit precision (equivalent to >133 bits)
  To reduce impact of scaling given lack of floating-point hardware
Had a fast “anticipating” carry
  Mechanical version of pass-transistor carry propagate used in CMOS adders (and earlier in relay adders)

## Slide 30: آدا لاولیس (1815-1852)
Ada Lovelace (1815-1852)
Translated lectures of Luigi Menabrea who published notes of Babbage’s lectures in Italy
Lovelace considerably embellished notes and described Analytical Engine program to calculate Bernoulli numbers that would have worked if AE was built
  The first program!
Imagined many uses of computers beyond calculations of tables
  بسیاری از کاربردهای رایانه را فراتر از محاسبه جداول تصور کرد
Was interested in modeling the brain

## Slide 31: ماشین حساب های اولیه قابل برنامه ریزی
Analog computing was popular in first half of 20th century as digital computing was too expensive
But during late 30s and 40s, several programmable digital calculators were built (date when operational)
  Atanasoff Linear Equation Solver (1939)
  Zuse Z3 (1941)
  Harvard Mark I (1944)
  ENIAC (1946)

## Slide 32: Atanasoff-Berry Linear Equation Solver (1939)
Fixed-function calculator for solving up to 29 simultaneous linear equations
Digital binary arithmetic (50-bit fixed-point words)
Dynamic memory (rotating drum of capacitors)
Vacuum tube logic for processing
In 1973, Atanasoff was credited as inventor of “automatic electronic digital computer” after patent dispute with Eckert and Mauchly (ENIAC)

## Slide 33: Zuse Z3 (1941)
Built by Konrad Zuse in wartime Germany using 2000 relays
Had normalized floating-point arithmetic with hardware handling of exceptional values (+/- infinity, undefined)
  1-bit sign, 7-bit exponent, 14-bit significand
64 words of memory
Two-stage pipeline 1) fetch&execute 2) writeback
No conditional branch
Programmed via paper tape
Replica of the Zuse Z3 in the Deutsches Museum, Munich

## Slide 34: Harvard Mark I (1944)
Proposed by Howard Aiken at Harvard, and funded and built by IBM
Mostly mechanical with some electrically controlled relays and gears
Weighed 5 tons and had 750,000 components
Stored 72 numbers each of 23 decimal digits
Speed: adds 0.3s, multiplies 6s, divide 15s, trig >1 minute
Instructions on paper tape (2-address format)
Could run long programs automatically
Loops by gluing paper tape into loops
No conditional branch
Although mentioned Babbage in proposal, was more limited than analytical engine

## Slide 35: ENIAC (1946)
First electronic general-purpose computer
Construction started in secret at UPenn Moore School of Electrical Engineering during WWII to calculate firing tables for US Army, designed by Eckert and Mauchly
17,468 vacuum tubes
Weighed 30 tons, occupied 1800 sq ft, power 150kW
Twelve 10-decimal-digit accumulators
Had a conditional branch!
Programmed by plugboard and switches, time consuming!
Purely electronic instruction fetch and execution, so fast
  10-digit x 10-digit multiply in 2.8ms (2000x faster than Mark-1)
As a result of speed, it was almost entirely I/O bound
As a result of large number of tubes, it was often broken (5 days was longest time between failures)

## Slide 36: EDVAC
ENIAC team started discussing stored-program concept to speed up programming and simplify machine design
John von Nuemann was consulting at UPenn and typed up ideas in “First Draft of a report on EDVAC”
Herman Goldstine circulated the draft June 1945 to many institutions, igniting interest in the stored-program idea
  But also, ruined chances of patenting it
  Report falsely gave sole credit to von Neumann for the ideas
  Maurice Wilkes was excited by report and decided to come to US workshop on building computers
Later, in 1948, modifications to ENIAC allowed it to run in stored-program mode, but 6x slower than hardwired
  Due to I/O limitations, this speed drop was not practically significant and improvement in productivity made it worthwhile
EDVAC eventually built and (mostly) working in 1951
  Delayed by patent disputes with university

## Slide 37: IBM 701 (1952)
IBM’s first commercial scientific computer
Main memory was 72 William’s Tubes, each 1Kib, for total of 2048 words of 36 bits each
  Memory cycle time of 12µs
Accumulator ISA with multipler/quotient register
18-bit/36-bit numbers in sign-magnitude fixed-point
Misquote from Thomas Watson Sr/Jr ( بنیان گذار IBM ):
“I think there is a world market for maybe five computers”
Actually TWJr said at shareholder meeting:
“as a result of our trip [selling the 701], on which we expected to get orders for five machines, we came home with orders for 18.”

## Slide 38: IBM 650 (1953)
The first mass-produced computer
Low-end system with drum-based storage and digit serial ALU
Almost 2,000 produced

## Slide 39: IBM 360 : A General-Purpose Register (GPR) Machine
The IBM 360 is why bytes are 8-bits long today!
Processor State
  16 General-Purpose 32-bit Registers
    may be used as index and base register
    Register 0 has some special properties
  4 Floating Point 64-bit Registers
  A Program Status Word (PSW)
    PC, Condition codes, Control flags
A 32-bit machine with 24-bit addresses
  But no instruction contains a 24-bit address!
Data Formats
  8-bit bytes, 16-bit half-words, 32-bit words, 64-bit double-words

## Slide 40
IBM Mainframes survive until today
2017